All materials used are T-6 Aluminium extrusions. All louvres are powdercoated to customers choice.

CARBOLITE Pty Ltd reserves the right to change or amend drawings without notice.

All materials used are T-6 Aluminium extrusions. All louvres are powdercoated to customers choice.

CARBOLITE Pty Ltd reserves the right to change or amend drawings without notice.

Bracket Fix:

# Text boxes

Wall Louvres Drawings –suits both 85mm elliptical blade/65mm slat

Componentry

- Channel        54mm x 32mm x 1.6mm

- Side Beam    50mm x 25mm x 1.8mm

- Slat               65mm x 16mm x 1.2mm

- Blade             85mm eliptical

- Side strip      48mm flat bar

- Screws

- Rivets

Angle of slats set at 56 degrees.

Side strip

Wall Mount Fixing

Bracket Sizes

- 100 x 100 x 6mm

- 150 x 150 x 6mm

- 200 x 200 x 6mm

- 250 x 250 x 6mm

Please note 1 bracket is needed per corner.

Componentry

1) Channel       54mm x 32mm x 1.6mm

2) Side Beam   50mm x 25mm x 1.8mm

3) Slat               65mm x 16mm x 1.2mm

4) Blade            85mm Eliptical

5) Side Strip      48mm Flat Bar

6) Screws

7) Rivets

Privacy screen Drawings - suits both 85mm elliptical blade/65mm slat

Side strip

Gap distance either 10mm or 20mm

Wall Mount Fixing

Bracket Sizes

- 100 x 100 x 6mm

- 150 x 150 x 6mm

- 200 x 200 x 6mm

- 250 x 250 x 6mm

Please note 1 bracket is needed per corner.

Cantilever Awning Drawings - suits both 85mm elliptical blade/65mm slat

Left Hand Bracket

Centre T Bracket

Right Hand Bracket

Louvre panel drops in between brackets.

Base plate dimension is subject to projection of louvre.

100

50

50

Bracket properties

Base plate    10mm aluminium

Flanges          6mm aluminium

Fixings          Per application

Max bracket span 2500mm

Max louvre span is 1500mm before stringer needed

Max. louvre span 1500mm before stringer

Max. louvre span 1500mm before stringer